## Slide 1: Regular Research Seminar
Feb 13th
2025298007
SuHan Yoon
E2E with Diffusion Model Planning

## Slide 2: TABLE OF CONTENTS
Experiment – Diffusion Planning
Introduce Diffusion-Planning
Diffusion-Planning’s Problem
Experiment Goal
Engineering – Autoware E2E
Introduce My Submission using Autoware
Comunication With Autoware
Engineering Goal

## Slide 3: Diffusion-Planner
Overview
Diffusion-Planner is a representative Transformer-based diffusion model for end-to-end trajectory planning.
Research Focus
Focuses on planning in end-to-end autonomous driving
Assumes perception (e.g., BEV representation) is already provided
Investigates trajectory generation and decision-making in complex driving scenarios
Dataset & Evaluation Environment
Evaluated on the nuPlan dataset
Uses closed-loop simulation for realistic planning evaluation
Experiment – Diffusion Planning

## Slide 4: Why Choose This Code?
1. Practical Planning Framework Implementation
Multi-modal Information Integration
  Beyond simple waypoint generation: integrates velocity profiles, acceleration, and surrounding vehicle states
  Generates actionable trajectories directly compatible with LQR controllers
2. Closed-Loop Evaluation-based Validation
Quantitative Assessment of Real-world Applicability
  Closed-loop reactive simulation on nuPlan benchmark
  Comparative analysis of rule-based refinement dependency (w/ vs. w/o post-processing)
  Real-world drivability validation ensuring practical deployability
Research Extensibility (Research Extrinsic Value)
Methodological Alignment with Generative AI
  Shares identical mathematical framework with image generation diffusion models (DALL-E, Stable Diffusion)
  Application of score-based generative modeling principles to motion planning
Experiment – Diffusion Planning

## Slide 5: Research Hypothesis
Experiment – Diffusion Planning
Problem Statement
Diffusion-Planner shows performance degradation in high lateral acceleration scenarios
Current Performance (nuPlan benchmark):
BenchMark | NR | R
Val14 | 89.87 | 82.80
Test14 | 89.19 | 82.93
Test14-hard | 75.99 | 69.22
Benchmark score of diffusion-planner
*NR : Non-Reactive Obstacle
*R : Reactive Obstacle
Root Cause Analysis
1. Data Imbalance
Dataset predominantly contains straight-driving scenarios
Insufficient examples of high-curvature maneuvers (lane changes, sharp turns)
2. Inadequate Curvature-Velocity Modeling
Velocity and curvature treated as independent continuous variables
Fails to capture speed-curvature coupling in human driving behavior
3. Training Objective Limitations
Behavior cloning cannot learn recovery from mistakes
No explicit optimization for safety constraints and comfort
Significant drop

## Slide 6: Solution 1. Data Reweighting – In Progress
Experiment – Diffusion Planning
Problem:
Dataset imbalance causes poor learning on high-curvature scenarios
Solution:
Increase sample weights for curve driving and lane changes
Expected: Improved lateral acceleration at high speeds
Goal: Improve test-14 benchmark success rate

## Slide 7: Solution 2. Velocity Discretization - In Progress
Experiment – Diffusion Planning
Problem:
Velocity-curvature variables have wide range; exact values less important than range-based patterns
High-speed needs diverse patterns; low-speed needs precision
Solution:
Split data into 3 categories:
  Accurate data (low-speed, precise control)
  Accurate + sampling (mid-speed, balanced)
  Sampling (high-speed, diverse patterns)
Apply curvature-velocity coupled discretization

## Slide 8: Solution 3. GRPO Fine-tuning
Experiment – Diffusion Planning
Solution:
Apply RL-based fine-tuning method developed by DeepSeek
Stage-wise learning:
  Path following
  Speed control
  Safety enhancement
Goal:
Improve test-14 benchmark success rate

## Slide 9: Solution 4. Curvature-Velocity Coupling Enhancement
Experiment – Diffusion Planning
Problem:
Model fails to properly adjust speed in high-curvature sections
Solution:
Explicitly model curvature-velocity joint distribution in diffusion conditions
Learn automatic deceleration behavior at high curvature

## Slide 10: Final Goal
Experiment – Diffusion Planning
1. Model Output Enhancement
Current: Position-heading trajectory (x, y, θ)
Proposed: Velocity-integrated trajectory (x, y, θ, v)
→ Enable explicit speed control along planned path
2. Target Performance
Benchmark: nuPlan Test14-hard (Reactive mode)
Baseline: 69.22
Target: ≥71.22 (+2.0 points improvement)
3. Focus Area
Reactive obstacle avoidance scenarios
High lateral acceleration maneuvers
→ Validate curvature-velocity coupling effectiveness
BenchMark | NR | R
Val14 | 89.87 | 82.80
Test14 | 89.19 | 82.93
Test14-hard | 75.99 | 69.22
Benchmark score of diffusion-planner
*NR : Non-Reactive Obstacle
*R : Reactive Obstacle

## Slide 11: Comunication with Autoware developer
Development Progress & Issues Report to Autoware Comunication
Objective:
  Development of an Autoware-based package generating High-Level Commands (HLC).
  Implementation of a hybrid methodology fusing Rule-Based algorithms and End-to-End (E2E) learning.
Current Technical Challenges:
  Hardware & Performance Limitations:
    Experienced computational resource insufficiency leading to critical data bottlenecks.
  Algorithmic Constraints:
    Addressed fundamental architectural issues inherent to the VAD (Vectorized Autonomous Driving) model.
Engineering – Autoware E2E

## Slide 12: WHY THE DELAY IN REPORTING?
Delayed Response Due To:
CES: Limited resources for immediate feedback
E2E: Focused on Autoware platform integration
with alpamayo
Engineering – Autoware E2E

## Slide 13: To DO
Retrain based on GenAD (6 days remaining)
Quantify DL4AGX improvements for justification
  Key considerations:
    Quantify deployment constraints with TensorRT
    GenAD requires VAD foundation (Uniad not supported)
    If Autoware integration succeeds: research FPS optimization (>10) and data collection methods
Engineering – Autoware E2E