## Slide 1: Regular Research Seminar
Jan 29th
2025298007
SuHan Yoon
E2E with Diffusion Model Pallnning

## Slide 2: TABLE OF CONTENTS
Research Goal & Workflow
Exploring Diffusion-based papers
Training DiffusionDrive v2
Training Diffusion-Planner
Developed MLOps Infrastructure

## Slide 3: main research directions for E2E autonomous driving based on my analysis
Explainable E2E with LLM/VLM
  Use VLM & LLM to generate semantic explanations of driving decisions
  Goal: improve transparency and human understanding
Perception Backbone Modification
  Investigate different backbone architectures for perception
  Analyze their impact on E2E driving performance
Planning Head Inference Strategy
  Modify the planning head architecture and inference mechanism
  Apply reinforcement learning-based fine-tuning to improve planning decisions
Research Goal & Workflow
My Interest
1

## Slide 4: Motivation: Why Diffusion-based Planning?
Diffusion models have demonstrated outstanding performance in generating complex structured outputs, particularly in image generation tasks (e.g., Nano Banana, Sora, Stable Diffusion).
Unlike conventional planning methods that rely on direct regression or candidate selection, diffusion-based planning enables multimodal trajectory generation and uncertainty modeling.
The denoising-based generation process makes diffusion models well-suited for producing structured trajectories and paths.
Furthermore, diffusion-based planners are more amenable to reinforcement learning fine-tuning compared to existing planning approaches such as VAD and UniAD, allowing direct optimization of planning quality.
Research Goal & Workflow
2

## Slide 5: Auto regressive vs Diffusion-based Generation
Conventional Autoregressive (Regression-based)
Predicts outputs sequentially (one step at a time)
Tends to produce mean predictions under multimodal distributions
Error accumulates over time
Limited ability to generate diverse trajectories
Diffusion-based Generation
Refines the entire trajectory simultaneously through denoising
Generates structured trajectories by sampling from a distribution
Preserves global consistency
Enables multimodal and robust planning
Research Goal & Workflow
Auto Regressive's Loss Rate
3

## Slide 6: Two Axes of DiffusionDrive: U-Net and Transformer
Concept (Architecture & Principle)
U-Net is a CNN-based encoder–decoder architecture with skip connections.
It performs denoising on spatial representations by learning both global and local features through downsampling and upsampling.
Planning is formulated as a spatial reconstruction (denoising) problem.
Input / Output Representation
Input: BEV map (2D grid) with noisy anchor paths
Output: Refined collision-free path
Noise → Clean Path
Learning Strategy (Anchor-based Refinement)
Instead of generating paths from scratch, U-Net refines predefined anchor trajectories through iterative denoising.
Anchors provide spatial references, enabling stable and efficient path generation.
Advantages
Requires relatively less training data compared to transformer-based models
Efficient inference due to CNN-based computation
Well-suited for spatial path generation in BEV space
Enables fast and stable local path planning
Research Goal & Workflow
4

## Slide 7: Two Axes of DiffusionDrive: U-Net and Transformer
Concept (Definition)
Transformer is the core deep learning architecture underlying large language models (LLMs).
It represents inputs as tokens and models their relationships using attention mechanisms.
Architecture & Principle
Uses self-attention to model relationships among trajectory tokens
Uses cross-attention to incorporate contextual information
Enables joint reasoning over multiple inputs without spatial constraints
Advantages for Autonomous Driving
Can jointly consider:
  spatiotemporal information
  vehicle states
  perception features
  high-level commands
Enables more accurate and consistent trajectory generation
Limitation
Computationally expensive due to attention operations
Unlike U-Net, there is no established anchor-based mechanism for reducing search space in autonomous driving planning
Research Goal & Workflow
5

## Slide 8: Comparison of Diffusion Models Based on U-Net and Transformer
Research Goal & Workflow
Aspect | U-Net-based Diffusion | Transformer-based Diffusion
Computation Cost | Fast inference with anchor-based refinement | Relatively high computational cost
Customization | Limited flexibility for architectural modification | Highly flexible and extensible architecture
Path / Trajectory Quality | Spatially valid local paths | Temporally consistent and context-aware trajectories
Representation | Spatial map (BEV, grid-based path) | Sequence of trajectory tokens
Reasoning Capability | Focused on local spatial structure | Capable of temporal and causal reasoning
Scalability | Efficient for real-time local planning | Suitable for complex multimodal planning
*These two approaches pursue different design philosophies, and it remains unclear which is universally superior.

## Slide 9: Introduce MY Base Source Code _ DiffusionDrive
Title : DiffusionDrive
Overview
DiffusionDrive is one of the most representative U-Net-based diffusion planning frameworks.
It evolves from previous works: SparseDrive → DiffusionDrive → DiffusionDriveV2.
  Design Philosophy
Focuses on optimization-oriented planning rather than large-scale model expansion
Emphasizes:
  small model size
  low training data requirement
  fast inference speed
  real-time performance
Research Goal & Workflow

## Slide 10: Introduce MY Base Source Code 2 _ Diffusion-Planner
Title : Diffusion-Planner
Overview
Diffusion-Planner is a representative Transformer-based diffusion model for end-to-end trajectory planning.
Research Focus
Focuses on planning in end-to-end autonomous driving
Assumes perception (e.g., BEV representation) is already provided
Investigates trajectory generation and decision-making in complex driving scenarios
Dataset & Evaluation Environment
Evaluated on the nuPlan dataset
Uses closed-loop simulation for realistic planning evaluation
Research Goal & Workflow

## Slide 11: Introduce MY Base Source Code's Feature
DiffusionDrive
Key Feature : Computationally efficient and lightweight architecture
Research Focus : Investigation of optimization strategies and reinforcement learning approaches for diffusion-based autonomous driving
Diffusion-Planner
Key Feature : Support for complex and flexible planning algorithms
Research Focus : Development of high-dimensional planning models integrating LLMs, VLMs, vehicle dynamics, and relative motion reasoning
Research Goal & Workflow

## Slide 12: My experiments Work Flow
Research Goal & Workflow
PC1.
4090
PC2.
H100
Learning Tools
Learning Code
MLOps
Versioning & Storge
Diffusion-Planner
DiffusionDrive
Preprocessed images
.pt
Check points
Git Version
Visualize & Distribute
Git : Code storge
Drive : Data storge
Tag & Save

## Slide 13: Dvc & DataBricks
MLflow (Databricks)
Used for experiment tracking and result visualization.
Manages metrics, models, and training logs in a centralized platform.
DVC (Data Version Control)
Integrated with GitHub for version control of both code and data.
Tracks and versions:
  Preprocessed images
  Training datasets
  Model checkpoints
  Experimental results
Objective
To build a portfolio that enables full reproduction of experiments.
All experimental settings, code, and results can be understood and verified from the portfolio alone.
Research Goal & Workflow

## Slide 14: Research Goal
Research Contribution Levels
  Major Contribution
  Reinforcement learning–based fine-tuning
  Modification of core algorithms
  Minor Contribution
  Network architecture and parameter tuning
  Engineering-oriented optimizatio
  Current Research Direction
    Focus on methods from:
    Computer Vision
    Large Language Models (LLMs)
    Rather than directly targeting autonomous driving–specific approaches
  Goal
  To surpass the benchmark scores reported in each reference paper
  Ensure fair comparison under identical experimental settings
  Demonstrate measurable performance improvements
Research Goal & Workflow

## Slide 15: Next Experiment
DiffusionDrive
Apply latent DDPM/DDIM-based image preprocessing methods.
Modify existing diffusion optimization algorithms used in prior work.
Investigate alternative optimization strategies for efficiency and performance improvement.
DiffusionPlanner
Reduce computational cost of Transformer-based architectures by combining CNN + Transformer models.
Explore LLM-based High-Level Control (HLC) for planning and decision-making.
Design lightweight and high-dimensional planning frameworks.
Research Goal & Workflow